# 6-Pin Phototransistor Output; GaAs Input

| référence | fab. | tension d'isolement | CTR à IF (% à mA) | tps de rép. (max.) | VF in (V max.) | IF in (mA max.) | Ic out (mA max.) | Vce out V max. | boîtier | broch. | commentaires | UdV | prix de l'U.D.V. €uros |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 canal |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CNW136 | Agilent | 1,2 kVRMS | 19-16 | 0,8 µs | 1,85 | 100 | 10 | 20 | DIP 8 | 5 | UL1577, | 1 | 2,09 |
|  |  |  |  |  |  |  |  |  |  |  | VDE0884. Vitesse = 1 Mbit/s. |  |  |
| TIL114 | TI | 2,5 kVpic | - | 10 µs | 1,4 | 100 | 7 (typ.) | 30 | DIP 6 | 3 |  | 1 |  |
| TIL116 | TI | 2,5 kVpic | - |  | 1,5 | 100 | 5 (typ.) | 30 | DIP 6 | 3 |  | 1 |  |
| TIL117 | TI | 2,5 kVpic | - | 10 µs | 1,4 | 100 | 9 (typ.) | 30 | DIP 6 | 3 |  | 1 |  |
| HCPL0501 | Agilent | 2,5 kVRMS | 19-16 | 0,8 µs | 1,7 | 20 | 8 | 30 | SO-8 | 5 | Vitesse = | 1 | 3,72 |
|  |  |  |  |  |  |  |  |  |  |  | 1 Mbit/s. |  |  |
| SL5501 | QTC | 2,5 kVRMS | 15-2 | 50 µs | 1,3 | 60 | 100 | 30 | DIP 6 | 3 |  | 1 | 0,89 |
| SL5500 | QTC | 2,5 kVRMS | 40-2 | 50 µs | 1,3 | 60 | 100 | 30 | DIP 6 | 3 |  | 1 |  |
| HCPL4562 | Agilent | 2,5 kVRMS | 45 (typ)-6 | - | 1,6 | 12 | 16 | 20 | DIP 8 | 5 | Analogique | 1 | 2,36 |
|  |  |  |  |  |  |  |  |  |  |  | large bande et vidéo ; non-linéarité = 0,25%, bande passante = 6 MHz. |  |  |
| IL205A | Siemens | 2,5 kVRMS | 40-10 | - | 1,5 | 60 | 50 | 70 | SOIC-8 | 4 |  | 5 | 4,01 |
| IL206A | Siemens | 2,5 kVRMS | 63-10 | - | 1,5 | 60 | 50 | 70 | SOIC-8 | 4 |  | 5 | 4,01 |
| 6N135 | TI | 3 kV c.c. | 7-16 | 15 µs | 1,7 | 25 | 8 | 15 | DIP 8 | 5 | Analogique | 1 |  |
|  |  |  |  |  |  |  |  |  |  |  | (BP = 2 MHz), numérique |  |  |
| 6N136 | TI | 3 kV c.c. | 19-16 | 0,8 µs | 1,7 | 25 | 8 | 15 | DIP 8 | 5 | Analogique | 1 |  |
|  |  |  |  |  |  |  |  |  |  |  | (BP = 2 MHz), numérique (Vitesse = 1 Mbits/s). |  |  |
| CNX35 | QTC | 3,12 kVRMS | 15-2 | 20 µs | 1,5 | 100 | 100 | 30 | DIP 6 | 3 |  | 1 | 0,68 |
| CNX36 | QTC | 3,12 kVRMS | 15-2 |  | 1,5 | 100 | 100 | 30 | DIP 6 | 3 |  | 1 | 0,80 |
| TIL126 | TI | 5 kVpic | - | 20 µs | 1,4 | 100 | 9 (typ.) | 30 | DIP 6 | 3 |  | 1 |  |
| 4N25 | Siemens | 5,3 kV c.c. | 12,5-16 | - | 1,5 | 60 | - | 30 | DIP 6 | 3 |  | 5 | 3,38 |
| CNY17-2 | Siemens | 5,3 kVRMS | 63-10 | - | 1,25 | 60 | 50 | 70 | DIP 6 | 3 |  | 5 |  |
| CNY17-3-X001 | Siemens | 5,3 kVRMS | 100-10 | - | 1,25 | 60 | 50 | 70 | DIP 6 | 3 |  | 5 |  |
| PC817 | Sharp | 5 kVRMS | 50-5 | 18 µs | 1,4 | 50 | 50 | 35 | DIP 4 | 1 |  | 1 | 0,96 |
| OPI1264B | Optek | 10 kV c.c. | 50-10 | 15 µs | 1,6 | 40 | - | 30 | 4 broches | - | UL n0E58730. | 1 | 3,99 |
| 2 canaux |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ISD74 | Optek | 1,5 kV c.c. | 12,5-16 | - | 1,5 | 60 | - | 20 | DIP16 | 7 |  | 1 | 2,00 |
| HCPL2530 | Agilent | 2,5 kVRMS | 7-16 | 1,5 µs | 1,7 | 25 | 8 | 20 | DIP 8 | 8 | App. anal. large | 1 | 7,15 |
|  |  |  |  |  |  |  |  |  |  |  | bande et numérique Vit. = 1 Mbits/s. |  |  |
| HCPL2531 | Agilent | 2,5 kVRMS | 19-16 | 0,8 µs | 1,7 | 25 | 8 | 20 | DIP 8 | 8 | App. anal. large | 1 | 3,69 |
|  |  |  |  |  |  |  |  |  |  |  | bande et numérique Vit. = 1 Mbits/s. |  |  |
| ILD205 | Siemens | 2,5 kVRMS | 40-10 | - | 1,55 | 30 | - | 70 | SOIC-8 | 9 |  | 1 | 2,08 |
| PC827 | Sharp | 5 kVRMS | 50-5 | 18 µs | 1,4 | 50 | 50 | 35 | DIP 8 | 9 |  | 1 | 1,58 |
| PC829 | Sharp | 5 kVRMS | 50-5 | 15 µs | 1,4 | 50 | 50 | 35 | DIP 8 | 7 |  | 1 | 1,73 |

# Optocoupler Specification Definitions

# CTR (current transfer ratio): Ratio of the collector to the diode forward current IC/IF.

# IF: Current flowing through a diode from anode to cathode.

# BVCEO: Collector to emitter breakdown voltage with the collector open.

# BVCBO: Collector to base breakdown voltage with the emitter open.

# BVECO: Emitter to collector breakdown voltage with the base open.

# VCE(sat): Collector to emitter saturation voltage.

# tON/tOFF:Turn-on switching time; turn-off switching time.

# VISO: Isolation voltage rating in ACRMS (1 second rating).

# Agency Approvals: Safety agency approvals that correspond to the part number.

# IFT: Diode forward current (IF) required to cause the output to change states.

# VOL: Logic low output voltage.

# VCC: Operating supply voltage.

# CMH;CML: Common mode transient immunity at logic high level output; common mode transient immunity at logic low level output.

# IOH: Logic high output current.

# tPLH/tPHL: Propagation delay time to logic high output; propagation delay time to logic low output.

# ICCL: Current drawn from the supply at logic low output.

# VTM: On-state voltage.

# VDM: Blocking voltage.

# IDM: Off-state current.

# IH: Holding current.

# RDS(ON)/RDS(OFF): On-state output resistance; off-state output resistance.

# VBR: Breakdown voltage.

# IFT(OFF)/IFT(ON): Hysteresis ratio.

# VINH: Inhibit Voltage.